## Slide 1: Wine NMR Multitask Prediction
Ross Kunz
8/31/2021

## Slide 2: Data
Objective
  Predict the chemical analyte signal for multiple attributes
  Nuclear Magnetic Resonance (NMR) data for each sample
  No environmental predictors
Dimensions
  40 samples from globally locations
  8712 NMR measurements
  17 different responses
Larsen et al. "An exploratory chemometric study of 1H NMR spectra of table wines." Journal of Chemometrics: A Journal of the Chemometrics Society 20.5 (2006): 198-208

## Slide 3: Exploration
There may exist relationships between samples
  Far left: Europe
  Middle: Mediterranean / Australia
Strong relationships along diagonal for most variables
  Strong block of negative correlation values

## Slide 4: Data Problems
Extremely high-dimensional
Low sample space (40)
Multicollinearity between NMR features
Autocorrelation of the NMR with respect to PPM
Multitask learning problem
  Correlation exists between responses
Alignment predetermined through paper methodology
Larsen et al. "An exploratory chemometric study of 1H NMR spectra of table wines." Journal of Chemometrics: A Journal of the Chemometrics Society 20.5 (2006): 198-208

## Slide 5: Previous Solution
Partial Least Squares (PLS)
  Like Principal Component Regression
  Use of X and Y in projection
  Bread and butter of chemometrics
Iterative Partial Least Squares
  Extension of PLS
  Extensive search over all predictors for subset selection
Different number of factors (F) and predictors (spectral range)
Larsen et al. "An exploratory chemometric study of 1H NMR spectra of table wines." Journal of Chemometrics: A Journal of the Chemometrics Society 20.5 (2006): 198-208

## Slide 6: Proposed Solution
Penalized Least Squares
Multitask approach via sparse group lasso
  Elastic-net
    Multicollinearity
    Reduction in the total number of predictors
  Tuning the hyper-parameters via cross validation
  Grouped variable selection across all responses
  GLMNET
Optional:
  Use of raw NMR
  Perform Principal Component Regression (PCR)
Yuan, Han, et al. "Multitask learning improves prediction of cancer drug sensitivity." Scientific reports 6.1 (2016): 1-11.

## Slide 7: Performance
Multitask Elastic-Net
  Average RMSECV of 0.63
  Reduction in the predictor space by 93%
    Same predictors among all responses
 | iPLS | MEN
Glycerol | 0.92 | 0.97
Ethanol | 0.94 | 0.92
Lactic Acid | 0.96 | 0.96
Malic Acid | 0.94 | 0.97
Methanol | 0.75 | 0.95
Glucose | 0.86 | 0.94
Glycerol | 0.92 | 0.97
Ethanol | 0.94 | 0.92
Lactic Acid | 0.96 | 0.96
Malic Acid | 0.94 | 0.97
Methanol | 0.75 | 0.95
Glucose | 0.86 | 0.94

## Slide 8: Diagnostics
Visible pattern at higher values
  Potential non-linear effects
  May be also be due to environmental factors / category
Similar trend per predictor

## Slide 9: Potential follow-ons
There may exist non-linear effects based on residuals
  Generalized Additive Models
Not accounting for environmental factors
Sample size is not large enough for train/test/validation
Different methods of feature selection
  Non-convex methods SCAD
  Adaptive lasso for consistent selection
  Fused lasso for combining predictors

## Slide 10: code
Created a small R package with the S3 class in mind for overloading methods
  Load_wine: (R.matlab)
  Plot.wine: (leaflet, plotly, corrplot, protoclust)
  Fit_wine: (glmnet)
  Predict.wine
  Plot.wine_predict: (ggplot2)

## Slide 11: conclusions
Multitask learning provides improvement over iPLS (using the wine data)
  Higher and more interpretable
  Multitask learning has been shown to be valuable in oncology
Issues still may exist
  Environmental factors
  Potential non-linearities
  Only Gaussian (glmnet) potential (RMTL)

## Slide 12: Questions?
Thank you for your time and consideration of me joining the SomaLogic Group